## Slide 1: Physics 120B: Lecture 4
LCD Text Display
Keypads and Time Slicing
Interrupts

## Slide 2: 2×16 LCD
Typically 5×8 dots per character
Note 16 pins: indicator of common interface

## Slide 3: Typical LCD Unit pinout
pin | function | Arduino pin (shield)
1 | ground | GND
2 | +5 V | +5 V
3 | VEE (contrast via potentiometer between 0 and 5 V) | pot on shield
4 | RS (LOW = command; HIGH = data/characters) | 8
5 | RW (LOW = write; HIGH = read) | GND
6 | E (enable strobe: toggle to load data and command) | 9
7-14 | data bus | 4,5,6,7  D4,D5,D6,D7
15 | backlight +V | 
16 | backlight ground | 
Note that most features are accessible using only the 4 MSB data pins

## Slide 4: Arduino LCD Shield
Handy package, includes buttons, contrast pot, some pins/headers for other connections
  consumes Arduino pins 4, 5, 6, 7, 8, 9
  leaves 0, 1 for Serial, 2, 3, 10, 11, 12, 13
    fails to make pin 10 available on header, though

## Slide 5
contrast adjust
Arduino pin breakout
a few other pins
A1—A5 on “S”
buttons utilize A0 analog input

## Slide 6: Buttons
The buttons use a voltage divider tree to present an analog voltage to A0
  note “RIGTH” typo made it onto printed circuit board!
I measure the following:
  none: 4.95 V
  SELECT: 3.59 V
  LEFT: 2.44 V
  DOWN: 1.60 V
  UP: 0.70 V
  RIGHT: 0.0 V
Easily distinguishable

## Slide 7: LCD Datasheet
For behind-the-scenes control of the LCD display, see the datasheet
  http://www.physics.ucsd.edu/~tmurphy/phys120b/labs/doc/LCD_HD44780.pdf
Above is just one snippet of the sort of things within

## Slide 8: And one other snippet from LCD datasheet
Datasheets: they build character (at least characters)

## Slide 9: The LiquidCrystal Library
This is one place I’m not itching for low-level control
  or wait—where’s the fun/challenge in that attitude?
Library makes simple
#include <LiquidCrystal.h>
LiquidCrystal lcd(8, 9, 4, 5, 6, 7); // matches shield config
void setup() {
lcd.begin(16, 2); // # columns & rows
lcd.print("Phys 120B Rules!");
}
void loop() {
lcd.setCursor(0, 1); // first col, second row (0 base)
// print the number of seconds since reset:
lcd.print(millis()/1000);
}

## Slide 10: The setup call
Arguments in LiquidCrystal type are:
  pins corresponding to: RS, Enable, D4, D5, D6, D7
  don’t need shield at all; just those 6 pins and power/gnd
  here’s one without shield: must hook R/W to gnd; rig pot

## Slide 11: Same thing in schematic form
Note this pinout is different than shield’s mapping

## Slide 12: Explore the library
Can do a lot with a few functions, but more available
  LiquidCrystal() must use
  begin() must use
  clear()
  home()
  setCursor() almost certainly use
  write()
  print() almost certainly use
  cursor()
  noCursor()
  blink()
  noBlink()
  display()
  noDisplay()
  scrollDisplayLeft()
  scrollDisplayRight()
  autoscroll()
  noAutoscroll()
  leftToRight()
  rightToLeft()
  createChar()

## Slide 13: LCD References
Good general intro to LCD control
  http://spikenzielabs.com/SpikenzieLabs/LCD_How_To.html
Arduino page
  http://arduino.cc/en/Tutorial/LiquidCrystal
See links on course site:
  http://www.physics.ucsd.edu/~tmurphy/phys120b/labs/useful_links.html
    http://www.physics.ucsd.edu/~tmurphy/phys120b/labs/doc/LCD-shield-schem.pdf
    http://www.physics.ucsd.edu/~tmurphy/phys120b/labs/doc/LCD_HD44780.pdf

## Slide 14: Keypads
Most keypads are matrix form: row contact and column contact
  pressing button connects one row to one column
note crossings do not connect:
dots indicate connection

## Slide 15: Reading the keypad
Imagine we hooked the rows (Y) to four digital inputs with pull-up resistors
  and hooked the columns (X) up to digital outputs
Now cycle through X, putting each to zero (LOW) in turn
  otherwise enforce high state
Read each row value and see if any inputs are pulled low
  means switch closed, button pressed
Called time-slicing
+5
+5
+5
+5

## Slide 16: Those Pesky Pullups
Arduino has a pinMode option to engage internal pullup resistors
  pinMode(pin, INPUT_PULLUP);
  does just what we want
Let’s start by defining our pins (example values)
  and our key characters
#define ROW1 12 // or whatever pin is hooked to row1
etc.
#define COL1 8
etc.
#define ROWS 4
#define COLS 4
char keys[ROWS][COLS] = { // handy map of keys
{'1','2','3','A'}, // black 4x4 keypad
{'4','5','6','B'},
{'7','8','9','C'},
{'*','0','#','D'}
};

## Slide 17: Now set up pins in setup()
Now in loop()
pinMode(ROW1, INPUT_PULLUP);
etc.
pinMode(COL1, OUTPUT);
etc.
digitalWrite(COL1, HIGH); // def. state is high; start high
pressed = 0; // value for no press
digitalWrite(COL1, LOW); // assert col 1 low
if (digitalRead(ROW1) == LOW)
pressed = 0x11; // upper digit is row
if (digitalRead(ROW2) == LOW)
pressed = 0x21; // lower digit is col
etc.
digitalWrite(COL1, HIGH); // reset col1 to high
etc. for all 4 columns; the scheme for pressed is just one way, my first impulse

## Slide 18: Piecing together at end of loop
print only if new press, new line if ‘#’ pressed
  note >> bit shift row look at high nibble;
  and mask lower 4 bits for isolating lower nibble
  thus decode into row and column (at least this is one way)
if (pressed != 0 && pressed != last)
{
row = pressed >> 4; // drop 4 LSB, look at upper 4
col = pressed & 0x0f; // kill upper 4 bits; keep 4 LSB
ch = keys[row-1][col-1]; // what character, from map
if (ch != '#’) // treat # as newline
Serial.print(ch);
else
Serial.println(""); // just want return
}
last = pressed; // preserve knowledge
delay(40); // debounce delay

## Slide 19: Cleaning up code
Repeating the sweep four times during the loop is a bit clumsy, from a coding point of view
  begs to be function()-ized
int readCol(int column)
{
int row_press = 0;
digitalWrite(column, LOW);
if (digitalRead(ROW1) == LOW)
row_press = 1;
if (digitalRead(ROW2) == LOW)
row_press = 2;
etc.
digitalWrite(column, HIGH);
return row_press;
}

## Slide 20: Now a function to sweep columns
int sweepCols()
{
int row_press;
pressed = 0;
row_press = readCol(COL1);
if (row_press > 0)
pressed = (row_press << 4) + 1;
etc.
row_press = readCol(COL4);
if (row_press > 0)
pressed = (row_press << 4) + 4;
return pressed;
}
now in main loop, just: pressed = sweepCols(); and otherwise same

## Slide 21: And, there’s a Library
Of course there is…
  http://playground.arduino.cc/code/Keypad
  installed in sketch folder libraries/ directory
#include <Keypad.h> const byte ROWS = 4; //four rows const byte COLS = 3; //three columns char keys[ROWS][COLS] = {{'1','2','3'}, {'4','5','6'},
{'7','8','9'}, {'#','0','*’}}; byte rowPins[ROWS] = {5, 4, 3, 2}; //conn. to the row pins of the keypad byte colPins[COLS] = {8, 7, 6}; //conn. to the col pins of the keypad Keypad keypad = Keypad( makeKeymap(keys), rowPins, colPins, ROWS, COLS ); void setup(){ Serial.begin(9600);} void loop(){ char key = keypad.getKey(); if (key != NO_KEY) Serial.println(key); }

## Slide 22: Some Notes on the Keypad Library
Note that the key map is taken seriously by Keypad.h
  if any character appears twice, it messes up
  therefore more than a printing convenience; a core functional element of the operation
Functions
  void begin(makeKeymap(userKeymap))
  char waitForKey()
  char getKey()
  KeyState getState()
  boolean keyStateChanged()
  setHoldTime(unsigned int time)
  setDebounceTime(unsigned int time)
  addEventListener(keypadEvent)
Consult link on previous slide for descriptions

## Slide 23: Combining LCD and Keypad?
The LCD uses six digital pins
A 4x4 keypad needs 8 pins
Uno has 14, but pins 0 and 1 are used by Serial
  could forgo serial communications, and max out pins
Need a better way, less greedy
Take a page from LCD shield buttons: use analog input
Many schemes are possible
  generally: +5 V on rows/cols, GND on other, resistors between
  could have all 16 buttons map to a single analog input
    interesting problem in designing appropriate network
  or make it easier and map to four analog inputs

## Slide 24: Four-Input Scheme
R1 thru R4 could be 10 kW, 4.7 kW, 2.2 kW, 1 kW
R5 thru R7 could be all 3.3 kW, or in that ballpark
  voltages will be 0 (nothing pressed), 1.25 V (top row), 2.06V; 3 V; and 3.8 V for resp. rows — lots of separation
Poll each A# input to ascertain keypress
+5
R1
R2
R3
R4
R5
R6
R7
R8
GND
A1
A2
A3
A4

## Slide 25: Interrupts
Sometimes we can’t afford to miss a critical event, while the main loop is busy, or in a delay, etc.
Interrupts demand immediate attention
Uno has two interrupts
  int.0 on pin 2; int.1 on pin 3
  Mega has 6 available interrupts
You can exempt some of loop from interruption
  may be rare that you need to do this, but…
void loop()
{
noInterrupts();
// critical, time-sensitive code here
interrupts();
// other code here
}

## Slide 26: Easily implemented
Just have to attach an interrupt to a service routine
  attachInterrupt(int#, function, trigger_type);
  the interrupt number is 0 or 1 on Uno (pins 2 or 3)
  the function is some function you’ve created to service the interrupt: name it whatever makes sense
  trigger_type can be
    RISING: detects edge from logic low to logic high
    FALLING: detects falling edge
    CHANGE: any change between high/low (watch out for bounce!)
    LOW: a low state will trigger an interrupt
  note that delay() will not work within the service routine
    need delayMicroseconds(), only good up to 16383 ms
    but not often interested in delay in interrupt routine

## Slide 27: Simple example
Turn on/off LED via interrupt; note volatile variable
int pin = 13; volatile int state = LOW; void setup() { pinMode(pin, OUTPUT); attachInterrupt(0, blink, CHANGE); } void loop() { digitalWrite(pin, state); } void blink() { state = !state; }

## Slide 28: Interrupt Notes
Inside the attached function, delay() won't work and the value returned by millis() will not increment. Serial data received while in the function may be lost. You should declare as volatile any variables that you modify within the attached function.
See the page for attachInterrupts():
  http://arduino.cc/en/Reference/AttachInterrupt

## Slide 29: Interrupts from analog?
What if we need to make a digital interrupt out of an analog signal like the analog-scheme keypad?
Can use a comparator to sense if we’re above or below some threshold voltage
  output is digital state
  could also use a high-pass (differentiator) to sense any significant change in the analog level, fed into a comparator

## Slide 30: Comparator Basics
Scheme is: when + input larger than − input, transistor driven to ON
  then current flows through transistor and output is pulled low
When Vin < Vref, Vout is pulled high (through the pull-up resistor—usually 1 k or more)
  this arrangement is called “open collector” output: the output is basically the collector of an npn transistor: in saturation it will be pulled toward the emitter (ground), but if the transistor is not driven (no base current), the collector will float up to the pull-up voltage
The output is a “digital” version of the signal
  with settable low and high values (here ground and 5V)
+

Vref
Vin
Vout
+5 V
R
5 V
Vref
Vout
Vin
time
V

## Slide 31: Can Gang Open-Collector Comparators into Chain
Put same (or different) threshold values on − inputs and four different analog signals on +
  tie all four open collectors together with common pull-up
  if any comparator activates, the associated transistor will pull the combined output low, and the other (off) transistors won’t care
The “311” comparator is standard
+

+

+

+


## Slide 32: Upcoming Lab
Monday is a holiday, so this is it for lab prep!
In Week 3 lab, we will:
  make an LCD analog voltage meter
  read a 4x4 keypad using the time-slice method and 8 pins
  combine the keypad, LCD, and interrupts into a party