## Slide 1: Physics 120B: Lecture 9
Project-related Issues

## Slide 2: Analog Handling
Once the microcontroller is managed, it’s often the analog end that rears its head
  getting adequate current/drive
  signal conditioning
  noise/glitch avoidance
    debounce is one example
  dealing with crude simplicity of analog sensors

## Slide 3: Computers are pretty dumb
Operating in the real world requires advanced pattern recognition
  the Achilles Heel of computers
  examples of failures/disappointments
    voice recognition (simple 1-D time series, and even that’s hard)
    autopilot cars?
    intolerance for tiny mistakes/variations
  many projects require discerning where a source is, avoiding obstacles, ignoring backgrounds, etc.
    just keep in mind that things that are easy for our big brains (which excel at pattern matching; not so good at tedious precision) may prove very difficult indeed for basic sensors and basic code

## Slide 4: Getting Enough Current
Some devices/sensors are not able to source or sink much current
  Arduino can do 40 mA per pin, which is big for this business
On the very low end, an op-amp buffer fixes many ills
  consider phototransistor hooked to 3 kW sensing resistor
  we’re talking mA of current, so drawing even 0.5 mA away from the circuit to do something else will change the voltage across the resistor substantially
  enter op-amp with inverting input jumped ‘round to output
  can now source something like 25 mA without taxing Vin one iota

+
Vin

## Slide 5: Transistor Buffer
In the hookup above (emitter follower), Vout = Vin  0.6
  sounds useless, right?
  there is no voltage “gain,” but there is current gain
  Imagine we wiggle Vin by V: Vout wiggles by the same V
  so the transistor current changes by Ie = V/R
  but the base current changes 1/ times this (much less)
  so the “wiggler” thinks the load is V/Ib = ·V/Ie = R
  the load therefore is less formidable
The “buffer” is a way to drive a load without the driver feeling the pain (as much): it’s impedance isolation
out
R
in
Vcc

## Slide 6: Push-Pull for Bipolar Signals
Sometimes one-sided buffering is not adequate
  need two transistors: npn for + side, pnp for −
  idea is that input sees high-impedance
  the current into the base is < 1/100 of ICE
  current provided by power supply, not source
Called a Push-Pull transistor arrangement
Only problem is “crossover distortion”
  npn does not turn on until input is +0.6 V
  pnp does not turn on until input is < −0.6 V
out
in
V+
V

## Slide 7: Hiding Distortion
Consider the “push-pull” transistor arrangement to the right
  an npn transistor (top) and a pnp (bot)
  wimpy input can drive big load (speaker?)
  base-emitter voltage differs by 0.6V in each transistor (emitter has arrow)
  input has to be higher than ~0.6 V for the npn to become active
  input has to be lower than 0.6 V for the pnp to be active
There is a no-man’s land in between where neither transistor conducts, so one would get “crossover distortion”
  output is zero while input signal is between 0.6 and 0.6 V
out
in
V+
V
crossover distortion

## Slide 8: Stick it into an op-amp feedback loop!
By sticking the push-pull into an op-amp’s feedback loop, we guarantee that the output faithfully follows the input!
  after all, the golden rule demands that + input =  input
Op-amp jerks up to 0.6 and down to 0.6 at the crossover
  it’s almost magic: it figures out the vagaries/nonlinearities of the thing in the loop
Now get advantages of push-pull drive capability, without the mess

+
Vin
out
V+
V
input and output
now the same

## Slide 9: Dogs in the Feedback
The op-amp is obligated to contrive the inverse dog so that the ultimate output may be as tidy as the input.
Lesson: you can hide nasty nonlinearities in the feedback loop and the op-amp will “do the right thing”

+
Vin
dog
inverse dog
“there is no dog”
We owe thanks to Hayes & Horowitz, p. 173 of the student manual companion to
the Art of Electronics for this priceless metaphor.

## Slide 10: MOSFETs often a good choice
MOSFETs are basically voltage-controlled switches
  n-channel becomes “short” when logic high applied
  p-channel becomes “short” when logic low applied
  otherwise open
Can arrange in H-bridge (or use pre-packaged H-bridge on a chip)
  so A=HI; A’=LOW applies VDD to left, ground to right
  B=HI; B’=LOW does the opp.
  A and A’ always opposite, etc.
  A and B default to LOW state

## Slide 11: Timing Issues
Microcontrollers are fast, but speed limitations may well become an issue for some
Arduino processor runs at clock speed of 16 MHz
  62.5 ns = 0.0625 ms
  machine commands take 1, 2, 3, or 4 cycles to complete
    see chapter 32 of datasheet (pp. 537−539) for table by command
  but Arduino C commands may have dozens of associated machine commands
    for example, digitalWrite() has 78 commands, though not all will be visited, as some are conditionally branched around (~36 if not PWM pin)
    testing reveals 4 ms per digitalWrite() operation (5 if PWM pin)
    implies about 64 (80) clock cycles to carry out

## Slide 12: Timing Exploration, continued
Program is basically repetitive commands, with micros() bracketing actions
  micros() itself (in 16 repeated calls, nothing between) comes in at taking 4 ms to complete
  Serial.print() takes 1040 ms per character at 9600 baud
    8 data bits, start bit, stop bit  10 bits, expect 1041.7 ms
    println() adds 2-character delay
  digitalRead() takes 4 ms per read
  analogRead() takes 122 ms per read
Also keep in mind 20 ms period on servo 50 Hz PWM
And when thinking about timing, consider inertia
  might detect obstacle 5 cm ahead in < 1 ms, but can you stop in time?

## Slide 13: Another Way to Explore Timing
Don’t be shy of using the oscilloscope
  a pair of digitalWrite() commands, HIGH, then LOW, will create a pulse that can be easily triggered, captured, and measured
  for that matter, you can use digital output pins expressly for the purpose of establishing relative timings between events
  helps if you have to choreograph, synchronize, or just troubleshoot in the time domain
  think of the scope as another debugging tool, complementary to Serial, and capable of faster information

## Slide 14: Control Problems
When it comes to controlling something through feedback, always think PID first
  PID: proportional, integral, derivative
control value:
error signal
desired output
actual output
subtract
add

## Slide 15: PID, in pieces
Proportional (Ghost of Conditions Present)
  where are we now?
  simple concept: take larger action for larger error
  in light-tracker, drive more degrees the larger the difference between phototransistors
  higher gain could make unstable; lower gain sluggish
Integral (Ghost of Conditions Past)
  where have we been?
  sort of an averaging effect: error × time
  responds to nagging offset, fixing longstanding errors
  looking to past can lead to overshoot, however, if gain is too high
Derivative (Ghost of Conditions Future)
  where are we heading?
  damps changes that are too fast; helps control overshoot
  gain too high amplifies noise and can produce instability

## Slide 16: PID, in pictures
Impact of changing different gains, while others held fixed
  blue is desired response
  green is nominal case
    Kp = Ki = Kd = 1 in this case
  ideal values depend on system
P
I
D

## Slide 17: Tuning PID Control
See http://en.wikipedia.org/wiki/PID_controller
One attractive suggested procedure:
  first control the system only with proportional gain
  note ultimate gain, Ku, at which oscillation sets in
  note period of oscillation at this ultimate gain, Pu
  If dealing with P only, set Kp = 0.5Ku
  If PI control: set Kp = 0.45 Ku; Ki = 1.2Kp/Pu
  If full PID: Kp = 0.6Ku; Ki = 2Kp/Pu; Kd = Kp×Pu/8
Control Theory is a rich, complicated, PhD-earning subject
  not likely to master it in this class, but might well scratch the surface and use some well-proven techniques

## Slide 18: Announcements
Project Proposals due Friday, 2/8, in class
This week’s lab:
  could work on light-tracker (due by next week, 2/12, 2/13)
  could work on proposals with “consultants” at hand
Next week we’ll begin project mode, with new schedule